# Motor controller – for driving the auxiliary motors forward - backwards
# Sabertooth 2X12 Dual Motor Driver – 24V 12 A
https://www.robotgear.com.au/Product.aspx/Details/461-Sabertooth-2X12-Dual-Motor-Driver

#### AUD $147.95
Qty needed: 2 → 4 motors

Connections: Screw terminals (not micro-fit)
Communication: 1 wire from Roboteq
Control: Needs configuration and some programming
Mounting: Mounting holes, no housing
Also needed (Qty=1):
https://www.altronics.com.au/p/z6369-rs232-serial-to-ttl-converter/
https://www.altronics.com.au/p/p1017-prototyping-jumper-wires-mixed-for-breadboard-arduino/

# Cytron Dual Channel 10A DC Motor Driver – 25 V 10A MAX
https://www.iot-store.com.au/products/cytron-dual-channel-10a-dc-motor-driver
AUD $25.00
Qty needed: 2 → 4 motors
Connections: Screw terminals (not micro-fit)
Communication: 8 Wires from Roboteq
Control: Straightforward use with Digital outputs from Roboteq
Mounting: Mounting holes, no housing
Also needed (Qty=1):
https://www.banggood.com/8-Channel-24V-To-5V-Optocoupler-Isolation-Module-PLC-Signal-Level-Voltage-Conversion-Board-p-1202825.html?gmcCountry=AU&currency=AUD&createTmp=1&utm_source=googleshopping&utm_medium=cpc_elc&utm_content=frank&utm_campaign=pla-ele-diy-au-pc-0404&gclid=Cj0KCQiA28nfBRCDARIsANc5BFC1GwyERhy4tJ9mwUPAj2UffM9ZatutpcZH6Ssm53PWAI857CtixX8aAiEQEALw_wcB&cur_warehouse=CN

# Roboteq SDC2160 - Brushed DC Motor Controller, Dual Channel, 2 x 20A, 60V

https://www.roboteq.com/index.php/component/virtuemart/307/sdc2160-detail?Itemid=970

USD $250.00

Qty needed: 2 → 4 motors
Connections: Screw terminals (not micro-fit)
Communication: 2 Wires from Roboteq, CAN BUS
Control: CAN BUS from Roboteq, requires programming
Mounting: Mounting holes, housing
Note: Probably overkill
Voltage Regulator:

24V	V (v)	I (A)	qty	Sub
Nidec 404 682 x 4	24	3.5	1	3.5	http://nidec-ma.de/en/productlist.html
Brake ???	24	2	1	2
Lights	24			0
Roboteq	24	0.1	1	0.1
Servo Nide 404.854	24	6	1	6
				> 10 A	240 W

# B70SR24125CC
24V, In: 36- 106V, 12.5A, 300W

https://www.digikey.com.au/product-detail/en/delta-electronics/B70SR24125CC/941-1809-ND/7681586
Includes an Enable/Disable signal useful for saving power and lifespan
AU$209.02

Dim: 190.0mm x 75.9mm x 43.9mm

B62SR24015CC
24V, 360W, 15A

https://www.digikey.com.au/product-detail/en/delta-electronics/B62SR24015CC/1145-1283-ND/9598967

Includes an Enable/Disable signal useful for saving power and lifespan

AUD $272.00

Connection: Molex Mini Fit (Included)
Dim: 190.0mm x 76.0mm x 44.0mm

# SD-350C-24
https://www.digikey.com.au/product-detail/en/mean-well-usa-inc/SD-350C-24/1866-4431-ND/7706520
350W, 14.6 A
AU$135.60
Input: 36- 72V
Dim: 215.0mm x 115.0mm x 50.0mm

Molex: Micro Fit, Male:
AU$3.70
https://www.digikey.com.au/product-detail/en/molex-llc/0430450829/WM10700-ND/3310210

Joystick

We can go to:
http://www.controldevices.net/P&G/Joysticks.html
http://www.controldevices.net/contactus.html

Option:
https://www.digikey.com.au/product-detail/en/apem-inc/HF11S10/1040-1098-ND/4291721
https://www.digikey.com.au/product-detail/en/apem-inc/505-442/1040-1041-ND/4246202

Lists:
https://www.digikey.com.au/products/en/switches/navigation-switches-joystick/204?k=joystick&k=&pkeyword=joystick&pv183=8063&pv276=4586&pv276=5&pv276=4660&pv276=4590&pv276=4591&pv69=6&pv69=4&pv69=225&pv697=200&pv697=11&pv697=51&pv697=10&pv697=53&pv697=110&sf=1&FV=1f140000%2Cffe000cc&quantity=&ColumnSort=1000011&page=1&pageSize=25

https://au.rs-online.com/web/c/switches/joystick-switches-accessories/joystick-switches/?applied-dimensions=4294508837,4294840285,4294877055,4294885167,4294880316,4294885351,4294885229